## Slide 1
Assessing Soil Erosion and Carbon Storage in Agricultural Soils: A Case Study in Ceylon Orchard Agro (Pvt) Ltd.
Pinsara.W.P.S1, Asha S. Karunaratne1, Eranga M. Wimalasiri1
1Department of Export Agriculture, Faculty of Agricultural Sciences,
Sabaragamuwa University of Sri Lanka

## Slide 2: Content for the Presentation
Introduction
Objectives
Material and Methods
Results and Discussion
Conclusion and Recommendations
References

## Slide 3
What is Soil Erosion?
Soil erosion is the process of wind and water moving soil particles from one location and transporting and depositing them elsewhere.
Introduction
Accelerate by humans
    Intensive agriculture
    Deforestation
    Cultivation on steep slopes
    Improper land management
Impacts
    Nutrient losses
    Loss of organic matters
    Runoff and siltation
    Food insecurity
Figure: Soil erosion process (Zafirah et al., 2017)

## Slide 4: Introduction
Soil Carbon Storage
Ability of terrestrial ecosystems to capture and store carbon in the form of soil organic matters, as well as dead and live vegetation covers.
Above ground biomass
Below ground biomass
Litter organic matter
Soil organic carbon

## Slide 5: Research Problem
Soil erosion is a major problem in sustainable soil management and to ensure food security
Therefore, it’s important for soil erosion to be assessed under future climate scenarios
Climate change has a direct impact on the soil erosion
Farmers been unconcerned about carbon storage in the farmlands
Soil carbon storage can improve the soil quality, soil health and productivity of the land

## Slide 6: Research objectives
Main objective
To assess the soil erosion and soil carbon storage using a modelling approach of InVEST model in the Ceylon Orchard Agro (Pvt) Ltd., under current (2001-2021) and future climate (2040-2099) scenarios
Specific objectives
To develop soil erosion potential map, total soil loss map, sediment retention map, sediment export map and total carbon storage map
To assess the changes of soil erosion with future climate under the climate change scenarios
To provide suggestions and recommendations to the plantation company to reduce soil erosion and improve soil quality

## Slide 7: Material and Methods
Study Area
The Ginganga Estate of Ceylon Orchard Agro (Pvt) Ltd.
Covers total of 88 acres
Low country wet zone (6.5944 N, 80.0154 E)
Average temperature: 24°C to 29.2°C
Average rainfall: (2380 mm)
Main crops:
  Oil palm
  Tea
  Cinnamon
  Cardamom
Figure: Map of the Study Area

## Slide 8
SDR Model
Carbon Model
Model description
Integrated Valuation of Ecosystem Services and Tradeoffs (InVEST) model - (version 3.12.0)
  To assess soil erosion - (InVEST) Sediment Delivery Ratio (SDR) model.
  To assess carbon storage - (InVEST) Carbon model
ArcGIS™ 10.8 mapping software (ArcMap 10.8)
Material and Methods

## Slide 9: Soil Erosion Assessment Inputs
InVEST SDR Model
Digital Elevation Model (DEM)
Rainfall Erosivity Factor(R) Map
Land Use Land Cover (LULC) Map
Biophysical Table
Watershed Map
Soil Erodibility Factor(K) Map

## Slide 10: 1. Digital Elevation Model (DEM)
Obtaining the relevant 30m x 30m DEM [United States Geological Survey (USGS)]
Processing the DEM using ArcGIS 10.8 clipping tool
Filling in sinks using ArcGIS 10.8 Filling Tool
Final DEM
Figure: DEM of study area

## Slide 11: 2. Rainfall Erosivity (R) Factor
Figure: R factor map for 2001-2021
Figure: R factor map for 2040-2069
Figure: R factor map for 2070-2099
Collecting monthly rainfall data (2001-2021/2040-2069/2070-2099)
Conversion of MAR into R factor map
R=(972.75 + 9.95 x MAR)/100
Preparing Mean Annual Rainfall (MAR) map using ArcGIS 10.8 IDW interpolation tool
R factor map

## Slide 12: 3. Soil Erodibility (K) Factor
Source: Piyathilaka et al
Soil Type | K factor
Alluvial Red yellow podzolic soil Red yellow podzolic soils and mountain regosols Reddish brown earths and low humic gley soils Reddish brown earths and immature brown loams Reddish brown earths with non-calcic brown Reddish brown earths and solodize solonetz Steep rockland and lithosols | 0.31 0.22 0.22 0.19 0.30 0.35 0.40 0.25
K factor map
Conversion of polygon map into raster map using ArcGIS 10.8 polygon to raster tool
Clipping study area using ArcGIS 10.8 Clipping Tool
Obtaining soil map of the Sri Lanka

## Slide 13: 4. Land Use Land Cover (LULC) Map
Figure: LULC map of study area
LULC map
Conversion of the polygon map into raster map using Feature of Polygon to Raster tool in ArcGIS 10.8
Editing Attribute table with LU description and LU code corresponding the biophysical table
Obtaining the Land Use/Land Cover (LULC) map for the study area

## Slide 14: 5. Biophysical table
LULC_NAME | usle_c | usle_p
cinnamon | 0.1 | 0.25
oil palm | 0.2 | 0.35
Cardamom | 0.1 | 0.25
cycle path | 0.001 | 0.001
Road | 0.001 | 0.001
ditch | 0.001 | 0.001
cycle path | 0.001 | 0.001
wire fence | 0.001 | 0.001
Building | 0.001 | 0.001
Water tank | 0.001 | 0.001
Well | 0.001 | 0.001
Culvert | 0.001 | 0.001
Electricity point | 0.001 | 0.001
Masonry drain | 0.001 | 0.001
Figure: LULC map of study area

## Slide 15: Carbon Storage Assessment
Carbon pools data
Above Ground Biomass
Below Ground Biomass
Soil Organic Matter
Dead Organic Matter
Carbon Storages for LULC types
InVEST Carbon Model
LULC Map
Total Carbon Storage Map
Carbon pools data - Global Forest Resources Assessment Report, FAO 2015

## Slide 16
Results and Discussion
Year | Soil Erosion Potential (t ha-1 year-1) |  | 
 | Mean | Maximum | Minimum
2001-2021 | 242 | 1885 | 3
2040-2069 | 202 | 1572 | 2
2070-2099 | 205 | 1587 | 2
1. Soil Erosion Potential (RKLS) Map
RKLS = R x K x LS x C x P
RKLS map for 2001-2021
RKLS map for 2040-2069
RKLS map for 2070-2099

## Slide 17: Results and Discussion
Year | Total Soil Loss (t ha-1 year-1) |  | 
 | Mean | Maximum | Minimum
2001-2020 | 10 | 188 | 0
2040-2069 | 8 | 157 | 0
2070-2099 | 8 | 158 | 0
2. Total Soil Loss (USLE) Map
USLE = R x K x LS x C x P
Total Soil Loss map for 2001-2021
Total Soil Loss map for 2040-2069
Total Soil Loss map for 2070-2099

## Slide 18: Results and Discussion
Year | Sediment Export (t ha-1 year-1) |  | 
 | Mean | Maximum | Minimum
2001-2020 | 1 | 21 | 0
2040-2069 | 1 | 17 | 0
2070-2099 | 1 | 18 | 0
3. Sediment export = USLE × SDR
Sediment export map for 2001-2021
Sediment export map for 2040-2069
Sediment export map for 2070-2099

## Slide 19: Results and Discussion
Year | Sediment Retention (t ha-1 year-1) |  | 
 | Mean | Maximum | Minimum
2001-2020 | 6 | 86 | 0
2040-2069 | 4 | 72 | 0
2070-2099 | 5 | 73 | 0
4. Sediment retention = K × LS(1 − CP)SDR
Sediment retention map for 2001-2021
Sediment export map for 2040-2069
Sediment export map for 2070-2099

## Slide 20: Results and Discussion
Figure: High slope of the study area

## Slide 21: Results and Discussion
Carbon Storage Mean values (t ha-1 ) | 
Total carbon storage | 60
Carbon storage in above ground biomass | 25
Carbon storage in soil | 19
Carbon storage in below ground biomass | 14
Carbon storage in dead organic matter | 2
Carbon Storage Assessment
Figure: Total carbon storage in study area

## Slide 22: Results and Discussion
Figure: Above ground biomass (25 t ha-1 )
2. Below Ground Biomass
Figure: Below ground biomass (19 t ha-1 )
1. Above Ground Biomass

## Slide 23: Results and Discussion
Figure: Soil organic matter (14 t ha-1 )
Figure: Dead organic matter (2 t ha-1 )
3. Soil Organic Matter
4. Dead Organic Matter
Agricultural Sciences Undergraduate Research Symposium 2023

## Slide 24: Conclusion and Recommendations
Total soil loss in the study area for baseline period (10 t ha-1), mid-century (8 t ha-1) end-century (8 t ha-1) can be categorized under medium soil erosion
Compared to the mid and end century, the research area experienced greater rainfall during the baseline period. So, compared to the other two periods, it can result in a higher average soil loss during the baseline period.
The total carbon storage of the study area is 60 t ha-1
Aboveground biomass is the dominant source of carbon among the main carbon pools according to the obtained carbon storage maps.

## Slide 25
Design conservation plans and management practices to reduce soil erosion
Further studies could be done using InVEST Water Yield Model (AWY) to estimate the relative contribution of water from different parts of the estate
Company could prepare a database with maps, results and descriptive statics of the study for future assessments
The company could use the output maps as monitoring tool for field observation
Suggestions

## Slide 26: References
Gunawan, G., Sutjiningsih, D., Soeryantono, H., Sulistioweni, W., 2013. Soil erosion estimation base on gis and remote sensing for supporting integrated water resources conservation management. Int. J. Technol. 4, 147–156.
https://doi.org/10.14716/ijtech.v4i2.110
Kumarasiri, A.D.T.N., Udayakumara, E.P.N., Jayawardana, J.M.C.K., 2021. Impacts of soil erosion and forest quality on water quality in Samanalawewa watershed, Sri Lanka. Model. Earth Syst. Environ. 8, 529–544. https://doi.org/10.1007/s40808-021-01082-y
Piyathilake, I.D.U.H., Sumudumali, R.G.I., Udayakumara, E.P.N., Ranaweera, L. V, Jayawardana, J.M.C.K., Gunatilake, S.K., 2021a. Modeling predictive assessment of soil erosion related hazards at the Uva province in Sri Lanka. Model. Earth Syst. Environ. https://doi.org/10.1007/s40808-020-00944-1
Perera, K.H.K., Udeshani, W.A.C., Piyathilake, I.D.U.H., Wimalasiri, G.E.M., Kadupitiya, H.K., Udayakumara, E.P.N., Gunatilake, S.K., 2020. Assessing soil quality and soil erosion hazards in the Moneragala District, Sri Lanka. SN Appl. Sci. 2. https://doi.org/10.1007/s42452-020-03926-1

## Slide 27
Acknowledgement
Prof. Asha S. Karunaratne (Internal Supervisor), Dean of Faculty of Agricultural Sciences , Sabaragamuwa University of Sri Lanka
Dr. Eranga M. Wimalasiri (Co supervisor), Module Coordinator, Agri Environmental Resource Management, Department of Export Agriculture, Faculty of Agricultural Sciences , Sabaragamuwa University of Sri Lanka
Mr. Samantha Liyanage (External supervisor), Director, Ceylon Orchard Agro (Pvt) Ltd, Ginganga estate, Udugama
Ms. Ovini Dissanayake, (Lecturer) Department of Export Agriculture, Faculty of Agricultural Sciences , Sabaragamuwa University of Sri Lanka

## Slide 28: Thank You!

## Slide 29
Figure: InVEST SDR model running interface
Figure: InVEST Carbon model running interface

## Slide 30
A = Annual soil loss (t (ha yr)−1)
R = Rainfall erosivity factor (MJ mm (ha hr yr)−1)
K = Soil erodibility factor (t ha hr (MJ ha mm) −1)
LS = Slope length-gradient factor (unitless)
C = Cover management factor (unitless)
P = Support practice factor (unitless)
A = R × K × LS × C × P
Assessment of Soil Erosion

## Slide 31
Sharma et al., 2010
Erosion intensity class

## Slide 32
Chart: 
| Baseline | Mid-century | End-century
Mean annual rainfall (mm) | 3194 | 2649 | 2680
Baseline 2001-2021
Mid-century 2040-2069
End-century 2070-2099
Mean Annual Rainfall
Figure: Mean annual rainfall of the study area

## Slide 33
Assessment of Soil Erosion and Carbon Storage
Field based method vs. Modelling approach
Field Based Methods
Modelling Approach
Labor intensive
Time consuming
Low data accessibility
Low reliability
High degree of flexibility
Time saving
Data accessibility
Convenient & inexpensive
Comparability of results