## Slide 1: Analysis of Energy Balance of the Teaching Farm of Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka
WMS Dhanapala1, GEM Wimalasiri1, EPRHHW Nilmalgoda2
1Department of Export Agriculture, Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka, Belihuloya, Sri Lanka
2Department of Biosystem Technology, Faculty of Technology, Sabaragamuwa University of Sri Lanka, Belihuloya, Sri Lanka

## Slide 2: Introduction
Energy is a driving force of existence and it is required for all agricultural activities.
Energy Input
Energy Output
Energy Loss
(Negative Energy Balance)
Energy Gain
(Positive Energy Balance)
Energy Input
Energy Output
Energy Balance
Energy Input
Energy Output
Agriculture
Energy

## Slide 3: Introduction cont..
LCA is a compilation and evaluation of the inputs, outputs and potential environmental impact of a product system through its life cycle (ISO 2004).
Sustainability assessment tool
Can be applied for any systems

## Slide 4: Objectives
Main Objective
To analyze the energy balance of crop and livestock production in the farm of the Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka using the Life Cycle Assessment (LCA) approach.
Specific Objectives
To assess the total energy input and output in crop and livestock production in the faculty farm.
To determine the Net Energy Ratio (NER) of crop and livestock production.
To determine the water use efficiency (WUE) of crop production in the faculty farm.

## Slide 5: Material and Methods
Study Area
Farm of the Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka.
Mid country intermediate zone (IM2)
(6.71488330 N, 80.78709490 E)
Figure 1: Map of the farm of the Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka

## Slide 6: Material and Methods
Data collection
Primary data
- Direct contact with farm manager, farm supervisor and
workers.
- Official records in the faculty farm (2020 to 2022
production period)
Secondary data
- Previously published literature

## Slide 7: Material and Methods
Crop production
18 crops have been selected to estimate the energy balance of crop production.
These crops are, coconut, banana, cassava, tea, okra, bean, long bean, wing bean, cabbage, radish, tomato, brinjal, thorn apple/elabatu (Solanum insanum), cucumber, snake gourd, luffa, rice and corn.

## Slide 8: Material and Methods

## Slide 9: Material and Methods
Livestock production
Cattle, goat, piggery and poultry unit have been selected to estimate energy balance of livestock production.

## Slide 10
Input
or
Output
(Kg)
Calculation
Energy Input
or
Energy Output
(MJ)
Co-efficient of energy factor
(MJkg-1)
X
Example –
Bean Seeds
1 kg
X
Energy Factor
14.9 MJ kg-1
=
Energy Input
14.9 MJ

## Slide 11
Calculation
Energy Input
Yan et al., (2020)
Where,
= Total energy inputs (MJ)
= Crop Type
= Number of crops
= Farm input
= Energy coefficient for the crop type
= Inputs of labor (h), male and female inputs with separate value
= Seeds (kg)
= Fertilizer (kg)
= pesticides (kg)
= Electricity for irrigation (kWh)
= Plastic films (kg)
= Diesel fuel (L)
= machinery (kg)

## Slide 12
Yan et al., (2020)
Energy Output
Where,
=Total energy outputs (MJ)
= Crop Type
= Number of crops
= Crop yield
= Energy coefficient of the crop type
= Crop grain (kg)
= Crop straw (kg)
= Crop root (kg)

## Slide 13
Yan et al., (2020)
Energy Balance

## Slide 14
Energy Input
Calculation
Yan et al., (2020)
Where,
= Energy Inputs (MJ)
= Livestock category
= Number of Livestock
= Feed types
= Number of feeds
= Feed inputs classified as
Energy coefficient value of the feed classified as
= Veterinary drug (kg)
= Human labor (h)
= Electricity consumption for the lighting of housing structures (kWh)
(4)

## Slide 15
Yan et al., (2020)
Where,
= Total energy outputs (MJ)
= Number of livestock
= livestock category
= Livestock yield
= Energy coefficient
,, andare carcass weight (kg), milk (kg), respectively.
(5)
Energy Output

## Slide 16
Energy Balance
Yan et al., (2020)

## Slide 17
Calculation
The Energy Balance and Net Energy Ratio
Yan et al., (2020)
Where,
Energy Balance (MJ)
Net Energy Ratio (Outputs/Inputs),
,,, and represent the same parameters as in the previous equations.

## Slide 18
Water Use Efficiency of Crop Production based on Energy
Yan et al., (2020)

## Slide 19: Results and Discussion
Crop production
Input Energy = 75.71 GJ (400.24 GJ ha-1)
Output Energy = 107.06 GJ (717.11 GJ ha-1 )
Energy Balance = -31.35 GJ (-316.87 GJ ha-1)
NER = 1.79
WUE = - 31.35 MJ m-3
Chart: Energy (GJ)
| Input energy | Output Energy
Energy (GJ) | 75.7063 | 107.0557
Figure 2:Energy Input and Output in Crop Production

## Slide 20: Results and Discussion
Livestock Production
Input Energy = 867.44 GJ
Output Energy = 108.70 GJ
Energy Balance = 758.73 GJ
NER = 0.13
Chart: Energy (GJ)
| Input Energy | Output Energy
Energy (GJ) | 867.437 | 108.703
Figure 3:Energy Input and Output in Livestock Production

## Slide 21
Crop and Livestock Production
Total Energy Input = 956. 36 GJ
Total Energy Output = 215.76 GJ
Energy Balance = 740.6 GJ
NER = 0.23
Chart: Energy(GJ)
| Input Energy | Output Energy
Energy (GJ) | 956.36 | 215.76
Figure 4:Total Energy Input and Output in Faculty Farm

## Slide 22: Conclusions
Crop production system in faculty farm shows the negative energy balance (-31.35 GJ ).
Livestock production system shows the positive energy balance (758.73 GJ).
Overall, there is a positive energy balance in the faculty farm (740.6 GJ)
WUE of crop production was - 31.35 MJ m-3

## Slide 23: Recommendations
This study can be further developed to calculate carbon footprint in the faculty farm
The analyzed data will be included into the database of the farm of the Faculty of Agricultural Sciences, Sabaragamuwa University of Sri Lanka.
Development of the data recording system and inputs management system in crop and livestock production in the faculty farm.

## Slide 24: References
Ozkan, Burhan, Handan Akcaoz, and Cemal Fert. 2004. “Energy Input-Output Analysis in Turkish Agriculture.” Renewable Energy 29 (1): 39–51. https://doi.org/10.1016/S0960-1481(03)00135-6.
Sefeedpari, Paria. 2012. “Assessment and Optimization of Energy Consumption in Dairy Farm: Energy Efficiency” 3 (3): 213–24. https://doi.org/10.5829/idosi.ijee.2012.03.03.
Yan, Zhengang, Fuqin Hou, and Fujiang Hou. 2020. “Energy Balances and Greenhouse Gas Emissions of Agriculture in the Shihezi Oasis of China.” Atmosphere 11 (8): 1–17. https://doi.org/10.3390/ATMOS11080781.
Yan, Zhengang, Fuqin Hou, and Fujiang Hou. 2020. “Energy Balances and Greenhouse Gas Emissions of Agriculture in the Shihezi Oasis of China.” Atmosphere 11 (8): 1–17. https://doi.org/10.3390/ATMOS11080781.

## Slide 25: Thank You